## Slide 1: Basic Design Parameters

## Slide 2
1
Estimated load consumption
2
Geographical distribution of consumers
5
Electric utility supply constraints
Page 3
Page 4
CONTENTS
Page 7
Factory production and operational constraints
Environmental conditions
4
3
6
Page 6
Page 5
About PMG Engineering
Regulatory constraints
#
Page 8
x

## Slide 3: Estimated Load Consumption
In order, to determine the total load consumption of a plant, all electrical consumers must be defined and listed by type. For example:
  Motors
  Electrical heaters (boilers, etc.)
  Lighting
  Computers and process control equipment
  Auxiliary sources
The total Installed Load (in kW) is derived by adding up the values of the installed power of all the equipment. The Installed Load represents the total load connected to the system but not necessarily the peak load that is operating at any given point in time, which will be less than the total Installed Load . In order to calculate the Consumed Load, the Installed Load must be multiplied by both the Simultaneity and Utilization factors. The Consumed Load should represent the maximum, or peak, operating load of a plant at any given point in time.
Notes: 3

## Slide 4: Geographical Distribution Of Consumers
Consumers should be grouped according to their facility/area/process. This will help in power distribution planning and in determining if additional secondary substations for specific areas are needed in additional to the primary substation.
Notes: 4

## Slide 5: Environmental Conditions
At the start of a project the engineer for an electrical project must define the environmental conditions in which the substation equipment will be operating. This information is a prerequisite to specifying the equipment, the type of structure, and the materials to be used, all of which have a direct influence on the cost of the installation.
Notes: 5

## Slide 6: Factory Production and Operational Constraints
In general, factories are designed to run continuously. The impact of any unintentional disruption to the electrical supply must be assessed in order to decide what action needs to be done.
This entails being aware of the power supply stability needs for each customer in terms of production and safety..
Notes: 6

## Slide 7: Electric Utility Supply Constraints
The design of an installation must take into account a number of constraints imposed by connection to a utility power distribution network.
The utility power supply may differ greatly in both size, capacity, and reliability from one region or country to another. It is therefore important to know the power supply options in a given location, particularly with regard to the method of connection and the quality of the electrical power supply.
It is also important to know the history of utility power reliability issues (frequency of outages) and power quality problems (transients, voltage sags, and harmonics) in order to plan for the addition of auxiliary sources to the power distribution network and to determine what additional equipment may be needed to compensate for the power quality and reliability issues.
Notes: 7

## Slide 8: Regulatory Constraints
In the case of an industrial project, the relevant electrical installation must be planned taking all relevant regulations/codes/standards into account in order to ensure conformance with relevant regulatory bodies.
Notes: 8