## Slide 1: Transformer

## Slide 2
1
Transformer
2
Working principle
5
Testing & maintenance
Page 3
Page 5
CONTENTS
Page 12
Types of transformer
Why are transformer needed?
4
3
x
Page 7
Page 6
About PMG Engineering
#

## Slide 3: Transformer
What is a transformer ?
Definition of transformer
Transformer is a static device which transforms a.c. electrical power from one voltage to another voltage keeping the frequency same by electromagnetic induction
Electrical power transformer is a static device which transforms electrical energy from one circuit to another without any direct electrical connection and with the help of mutual induction between two windings. It transforms power from one circuit to another without changing its frequency but may be in different voltage level.
Notes: 3

## Slide 4: Working principle
Working Principle
The working principle of transformer is very simple. It depends upon Faraday's law of electromagnetic induction. In actual, mutual induction between two or more winding is responsible for transformation action in an electrical transformer.
Main Constructional Parts of Transformer
  The three main parts of a transformer are, Primary Winding of Transformer- Which produces magnetic flux when it is connected to electrical source.
Magnetic Core of Transformer-
  The magnetic flux produced by the primary winding, that will pass through this low reluctance path linked with secondary winding and create a closed magnetic circuit.
Secondary Winding of Transformer: The flux, produced by primary winding, passes through the core, will link with the secondary winding. This winding also wounds on the same core and gives the desired output of the transformer.
Notes: 4

## Slide 5: Why are transformer needed?
A substation is a part of an electrical generation, transmission and distribution system. Substations transform voltage from high to low, or the reverse, or perform any of several other important functions. Between the generating station and consumer, electric power may flow through several substations at different voltage levels.
A substation may include transformers to change voltage levels between high transmission voltages and lower distribution voltages, or at the interconnection of two different transmission voltages.
Notes: 5

## Slide 6: Types of transformer
Types of transformer by application
Distribution transformer
Power transformer
Current transformer
Potential transformer
Furnace transformer
Booster transformer
Rectifier transformer
Notes: 6

## Slide 7: Types of transformer
Distribution transformer
Power transformer
A transformer is a static machine used for transforming power from one circuit to another without changing frequency. This is a very basic definition of transformer. Since there is no rotating or moving part so transformer is a static device. Transformer operates on ac supply. Transformer works on the principle of mutual induction.
The step-down transformers used for electric power distribution purpose are referred as distribution transformer. There are several types of transformer used in the distribution system. Such as single-phase transformer, three phase transformer, pole mounted transformer, pad mounted transformer, and underground transformer.
Notes: 7

## Slide 8: Types of transformer
Current transformer
Potential transformer
The Current Transformer ( C.T. ), is a type of “instrument transformer” that is designed to produce an alternating current in its secondary winding which is proportional to the current being measured in its primary. Based on the function performed by the current transformer, it can be classified is follows:
  Measuring current transformers.
  Protective current transformers.
Potential transformer or voltage transformer gets used in electrical power system for stepping down the system voltage to a safe value which can be fed to low ratings meters and relays. Commercially available relays and meters used for protection and metering, are designed for low voltage
Notes: 8

## Slide 9: TYPES OF TRANSFORMER
Furnace transformer
Booster transformer
An electric arc furnace the transformer has heavy copper bus for the low voltage winding, which can be rated for tens of thousands of amperes. They are immersed in oil for cooling and insulation and are designed to survive frequent short circuits.
Booster transformer is one which is often used towards the end of a power line to raise the voltage to the desired value. It is used for controlling the voltage of a feeder at a point far away from the main transformer.
Notes: 9

## Slide 10: Types of transformer
Rectifier transformer
A rectifier transformer is a transformer which includes diodes or thyristors in the same tank. Voltage regulation may also be included. Rectifier transformers are used for industrial processes which require a significant direct current (dc) supply. Typical processes would include dc traction, electrolysis, smelting operations, large variable speed drive trains, etc.
Notes: 10

## Slide 11: Testing & maintenance
Testing of transformer
Testing is carried out as per IS-2026 . routine, type tests & special tests.
  Measurement of winding resistance.
  Measurement of insulation resistance.
  Separate source voltage withstand test (High Voltage tests on HV & LV)
  Induced Over voltage Withstand test (DVDF test)
  Measurement of voltage ratio
  Measurement of no-load loss & current.
Indian standards on distribution transformers.
  IS 1180 (Part 1): 2014 - Outdoor type, insulated liquid immersed Distribution Transformers upto and including 2500 kVA, 33kV (Part 1: Mineral Oil Immersed)
Notes: 11

## Slide 12: Testing & maintenance
Maintenance of transformer
Power Transformers, their materials, components and how they operate. It also emphasizes the importance of transformer management life especially for those transformers which have been in operation for 20 years and more. The course will address in detail all aspects related to transformer principles, calculations, operation, testing and maintenance.
  Preventative maintenance
  General condition of breathers
  Oil analysis
  Thermal inspection
  Oil leaks
  Protection relays
  Tap changers settings
  Earthing
Notes: 12