## Slide 1: Electrical Network Design Methodology and Application

## Slide 2
1
Methodology and application
2
Stages of methodology
5
Power Sources of substation auxiliaries
Page 3
Page 4
CONTENTS
Page 8
Power Sources of substation auxiliaries
Classification of loads
4
3
6
Page 6
Page 5
About PMG Engineering
Earthing systems
#
Page 10
X

## Slide 3: Methodology and Application
Methodology and application
The profitability of an industrial installation is directly linked to the availability of the production tool.
Electrical networks supply the energy required for the production tool to operate. Thus, continuity of supply to loads is studied when the network is being designed and especially when the preliminary choices for the single-line diagram are being made.
The aim of designing an electrical network is to determine the electrical installation which will meet the requirements of the industrial process for the least investment, operation and failure cost.
The design methodology of a network has six main stages.
Notes: 3

## Slide 4: Stages of Methodology
Collection of data (stage 1)
Preparation of the preliminary single-line diagram (stage 2)
This involves preparing a single-line diagram which meets needs and obligatory requirements, and which takes all the data into account.
This involves:
  I dentifying problems, needs to be met and obligatory requirements.
  Collecting the elements required for designing the network and defining equipment.
Notes: 4

## Slide 5: Stages of Methodology
Technical studies and single-line diagram validation (stage 3)
This involves a validation and technical/economic optimisation study of the planned structure taking into account all the data and hypotheses. It requires network calculations (short-circuit currents, load flows, etc.) to be carried out
Choice of equipment (stage 4)
Once the single-line diagram has been validated, the equipment is chosen and sized using the results of the calculations carried out during the previous stage and the data collected during stage 1.
Notes: 5

## Slide 6: Stages of Methodology
Choice and setting of protection devices (stage 5)
This involves defining the protection devices allowing faults to be detected and cleared and protection settings to be determined.
Choice and installation of a control and monitoring system (stage 6)
This involves choosing the structure of the control and monitoring system that will enable users to control and monitor the network and which will include automatic processes optimising the cost and availability of energy:
  source changeovers
  load-shedding/restoration
  automatic reconfigurations of distribution loops etc.
Notes: 6

## Slide 7: Classification of Loads
Classification of loads
Load operating conditions
This involves listing the installation's loads by classifying them per type:
  Motor , Lighting , Heating etc.
for which the following must be known:
  nominal powers (active, reactive and apparent)
  power actually absorb cost
  efficiency - operating transients (motor starting, etc.)
  emitted and tolerated disturbance levels (harmonics, unbalance, flicker, interruptions)
There are three main operating cases:
  Loads which operate continuously throughout installation operation time
  Loads which operate intermittently in relation to installation operation time
  Load which do not operate during normal circumstances and which back up loads whose operation is vital for safety reasons and possibly for the industrial process.
Notes: 7

## Slide 8: Power Sources of Substation Auxiliaries
Loads which are linked to the electrical distribution
Protective relays, contact coils of contactors
Operating mechanisms carrying out opening and closing of circuit-breakers, switches and isolators
Air conditioning systems of electrical rooms or switchboards and anti-condensation resistors
Electrical room ventilator, electrical room lighting
Cooling radiators, fans and tap changers of transformers.
These loads must be supplied by specific sources having a high level of reliability.
Notes: 8

## Slide 9: If these sources are lost, two operating principles are used:
Substation tripping; this principle makes the safety of persons and equipment a priority
Non-tripping; this principle makes service continuity a priority.
Monitoring the state of these sources is essential.
Power Sources of Substation Auxiliaries

## Slide 10: Earthing Systems
Choice of MV network earthing systems
Choice of earthing systems in LV networks
Service continuity
Level of overvoltages generated
Risk of an electrically caused fire
Level of electromagnetic disturbances
Design and operation requirements.
Service continuity
Level of overvoltages generated
Equipment phase-earth insulation level
Thermal stress relating to the earth fault current value
Complexity of protections
Operation and maintenance requirements
Network size.
Notes: 10