## Slide 1: GASKET MANAGEMENT PROGRAM

## Slide 2: AGENDA
2
Scope
3
Benefits
4
Key Elastomeres in food manufacturing
5
Roles & Responsibilities
6
Risk Matrix & inspection frequency
7
Procedure
1
Purpose
Notes: 2

## Slide 3: PURPOSE
Why map gaskets?
Damaged/ broken gasket in the process area can lead to product contamination or can be a source of foreign body in the finished product.
Gasket mapping helps in risk analysis of gasket with respect to their suitability to the controls and risk generated from moving parts.
It also helps define the inspection frequency based on
  risk matrix,
  suitable type of gasket material and
  certifications required
Notes: 3

## Slide 4: SCOPE
Where is gasket mapping applicable?
The procedure is applicable to all processes in manufacturing / filling where gaskets are used, including offline equipment like tote bin, sieves etc.
Any gasket that comes in contact (direct or indirect) with food has to be mapped and assessed for risks on regular basis.
Notes: 4

## Slide 5: BENEFITS
Mapping of Gaskets helps to
Mitigate Foreign Body Incident Risk by:
  Usage of right gaskets at right place.
  Adequate inspection plan
  Reduction in Consumer Complaints
  Reduction in Cost of Non Quality
Notes: 5

## Slide 6: KEY ELASTOMERES IN FOOD MANUFACTURING
Key elastomers used in food manufacturing process
No | Elastomer Type | ASTM Designation | Process Medium |  |  | 
 |  |  | Vegetable Fats | Animal Fats | Acid | Alkali
1 | Nitrile | NBR | 1 | 1 | 2/3 | 1
2 | Hydrogenated Nitrile | HNBR | 1 | 1 | 2 | 1
3 | Ethylene Propylene | EPDM | 3 | 3 | 2 | 1
4 | Silicone | VMQ | 2 | 2 | 2 | 2
5 | Fluorocarbon | FKM | 1 | 1 | 2 | 3
4 | Perfluoelastomer | FFKM | 1 | 1 | 1 | 1
7 | CI or Br Butyl | ClIIR or BrIIR | 2 | 2 | 1 | 1
Notes: 6

## Slide 7: KEY ELASTOMERES IN FOOD MANUFACTURING
Key elastomers used in food manufacturing process
Key : 1 – Excellent; 2 – Good; 3 – Poor; 4 – Do not use
No | Elastomer Type | Operating Range OC | Process Medium |  |  | 
 |  |  | Hot Water | Steam (150 OC) | Ozone | UV
1 | NBR | -40 to +120 | 1 | 4 | 2/3 | 2
2 | HNBR | -30 to +180 | 1 | 1 | 2 | 2
3 | EPDM | -50 to +150 | 1 | 1 | 1 | 1
4 | Silicone | -60 to +200 | 1 | 3 | 1 | 1
5 | Fluorocarbon | -20 to +200 | 1/2 | 2 | 1 | 1
4 | Perfluoelastomer | -15 to +260 | 1 | 1 | 1 | 1
7 | CI or Br Butyl | -40 to +150 | 1 | 1 | 1 | 1
Notes: 7

## Slide 8: ROLES & RESPONSIBILITIES
Role | Responsibilities
Concerned operator/ Technician | Check/ replace gaskets as per inspection frequency Inform Shift in charge in case of any deviation.
Production Shift in Charge | Gasket Mapping & Risk Assessment Ensure checking of gaskets as per inspection frequency
Plant Engineer | Gasket Mapping & Risk Assessment. Ensure availability of gaskets in technical store as per right specifications and required certifications. Ensure checking of gaskets as per inspection frequency.
Factory Hygienist | Assist in gasket mapping and risk assessment. Lead periodic verification of adherence to the procedure
HOD’s (Engineering, Production & QA) | Approve gasket mapping of process and ensure system of gasket inspection / replacement is working properly. Ensure gasket is procured from recommended supplier only.
Notes: 8

## Slide 9: RISK MATRIX & INSPECTION FREQUENCY
No. | Risk of Moving Part | Subsequent Control* | Gasket (OEM/ PV/ SLV)* | Risk Rating | Inspection Frequency
1 | Yes | No | SLV | Very High | Monthly
2 | Yes | No | OEM/ PV | High | **Quarterly
3 | Yes | Yes | OEM/ PV/ SLV | Medium | Half Yearly
4 | No | No | OEM/ PV/ SLV | Low | Yearly
5 | No | Yes | OEM/ PV/ SLV | Very Low | Not Required
Risk of gaskets for determining the inspection frequency shall be analyzed using the matrix below:
OEM: Original Equipment Manufacturer PV: Preferred Vendor
SLV: Standard Local Vendor
Notes: 9

## Slide 10: PROCEDURE
Action | Description
Line Mapping | Prepare list of all gaskets used in production lines including: Gasket Material, Size, Existing Store Item No. (If any), Vendors (categorized as OEM / Preferred / Local). Responsibility of inspecting the gasket, whether production or engineering.
Risk Assessment | Risk assessment of all mapped gaskets should be done basis Criticality of gasket is decided basis: Subsequent controls in process line Position of gasket in process (Static / Moving) Further, inspection frequency is derived from Risk rating of gasket.
Notes: 10

## Slide 11: PROCEDURE
Action | Description
P&ID Update | P&ID’s will enable to have transparency that right gaskets is used at right place, for which, P&ID of all lines should be updated with information of gasket location on machinery along with store item number. This will also ensure ease of withdrawal from technical store in case of replacements. It is further recommended to mark these gaskets in separate colors for visual identification of High / Medium and Low risk. Further, all gaskets mapped on P&ID must bear their Store item codes.
Gasket Library | Having a gasket library will enable to have traceability & Root Cause Analysis in case of any incident. Gasket library should be prepared with a sample of such gasket marking the locations it is used on. Libraries should be kept at a centralized location in factory with Factory Hygienist.
Notes: 11

## Slide 12: PROCEDURE
Action | Description
Gasket Inspection | P&ID’s will enable to have transparency that right gaskets is used at right place, for which, P&ID of all lines should be updated with information of gasket location on machinery along with store item number. This will also ensure ease of withdrawal from technical store in case of replacements. It is further recommended to mark these gaskets in separate colors for visual identification of High / Medium and Low risk. Further, all gaskets mapped on P&ID must bear their Store item codes.
Gasket Library | Inspection of gaskets is to be performed once frequency is arrived basis Risk analysis. Inspection should be recorded in form of pictorial checklists and/ Maintenance plans. Where Pictorial checklists are being used for inspection, records should be maintained by Production & Engineering for their respective gaskets
Notes: 12

## Slide 13: PROCEDURE
Action | Description
Selection of gaskets | Following decision tree is mandatory while selecting gaskets
OEM
Preferred Vendor
Move to Preferred Vendor
Standard Local Vendor
Notes: 13

## Slide 14: PROCEDURE
Action | Description
Gasket Certification | When all data for gaskets is collected, identified Original Equipment Manufacturers must be contacted for providing Food Grade / Phthalate free certificates. In case OEM is unable to provide certificates for existing gasket, but provides a suitable replacement with certificates, the gasket must be re-ordered to OEM. Non-Standardized gaskets from Local vendors are to be mitigated as part of Gasket management exercise. Purchase of gaskets from such vendors should be converted to “Preferred vendors”. Preferred vendors are globally reputed vendors, such as Garlock, Sealmax (KWO & IDT Germany) etc. No gaskets however, should be accepted if certificates are not provided.
Attached below is template referenced in the above procedure that can be used for data collection and tracking of gaskets.
Notes: 14