## Slide 2: AGENDA
1
What is rework?
2
Handling Rework
3
Risk of mishandling rework
4
Rework Usage
5
Rework- Important Considerations
Notes: 2

## Slide 3: WHAT IS REWORK?
Rework
Rework is defined as product that has been recovered or rejected from normal production and has been reprocessed, re-blended, or reformatted into the finished product.
Rework is an unincorporated food product kept for subsequent use or reprocessing.
Examples of rework
Mixing production from one day into a batch from a different day
Re-forming meat patties rejected for being broken, underweight or improperly breaded
Reprocessing dough left over from previous production
Repacking cookies that were mislabeled
Notes: 3

## Slide 4: HANDLING REWORK
When handling rework
Identify the rework material: Apply tags with product identification information, which may include name of the product, lot code and date of production.
Store rework in a way that prevents contamination with potential food hazards and growth of micro-organisms
  Establish the maximum storage time for your rework material.
  Put controls in place to prevent storing rework material for long periods.
Prevent cross-contamination with allergens: Inappropriate use of rework materials may result in the presence of undeclared ingredients in final products.
  This may trigger allergic reactions in some people who are sensitive to a specific ingredient or product. To prevent cross contamination with potential allergens not listed on their labels you may
    specify designated uses for rework materials. For example, use rework materials only with products that already have the same ingredients
Notes: 4

## Slide 5: HANDLING REWORK
When handling rework
    specify designated uses for rework materials. For example, use rework materials only with products that already have the same ingredients
    Identify the rework material: Apply not listed on their labels you may
Establish the maximum amount of rework material allowable in a product to control the effect of rework on the final formulation. The amount of rework you add should not alter the nutrition content or the ingredient listing of the product.
Develop a rework tracking system to be able to identify the final products containing rework materials. A rework tracking system will be necessary if a food product is recalled because it or any of its ingredients is identified as a health risk. If a food product is suspected of presenting a potential hazard to the public, you will need to identify all of its raw materials and ingredients, including rework materials.
Notes: 5

## Slide 6: HANDLING REWORK
When handling rework
  To keep track of rework material
    develop a recording system for rework that includes the time, quantity and processing step it was collected from, the original lot or batch number/code and the code of the lot or batch it was added to
    record the use of rework material from a specific lot code/batch or production date on your daily production record
Train your staff. Make sure you communicate to your staff all the instructions and procedures on the use of rework and the risks associated with the mishandling of rework material. Post a copy of those procedures at the plant, if necessary.
Monitor the use of rework. To ensure rework material is used and handled properly, you should:
Notes: 6

## Slide 7: HANDLING REWORK
When handling rework
  confirm that rework material is properly identified
  confirm that rework material is stored under conditions that protect the safety of your products (ex: correct temperature)
  observe employees handling rework to ensure they follow proper procedures
  monitor your rework tracking system by reviewing records
Notes: 7

## Slide 8: RISK OF MISHANDLING REWORK
When handling rework
Mishandling rework material may result in potential hazards such as:
  presence of undeclared allergens due to cross-contamination — for example when a product containing a specific allergen is mixed with a product that does not contain the ingredient and labelling is not changed to acknowledge the fact.
  contamination with pathogenic bacteria due to improper personal hygiene or product handling practices
  growth of pathogenic bacteria due to temperature abuse — for example, rework material that requires refrigeration is left at room temperature overnight and used as an ingredient in the next day's production.
  growth of pathogenic bacteria due to time abuse — for example, rework material stored for long period of time due to improper stock rotation
  presence of undeclared restricted ingredients in the final product — for example, addition of cured meat to a fresh meat product, which should not contain curing agents
Notes: 8

## Slide 9: REWORK USAGE
While using rework
Where rework is incorporated as an “in‐process” step
  The acceptable quantity, type and conditions of rework use shall be specified.
Where rework activities involve removing a product from filled or wrapped packages
  Ensure the removal and segregation of packaging materials.
  Avoid contamination of the product with extraneous matter.
Notes: 9

## Slide 10: REWORK- IMPORTANT CONSIDERATIONS
Remember to consider
Impact of rework on lot identification
  Must have a clear break in production
Potential hazards associated with rework from lines processing multiple similar products
  Allergens
Notes: 10