## Slide 1: EQUIPMENT DESIGN

## Slide 2: AGENDA
1
Sanitary construction & design of food equipment
2
Food product contact services
3
Non product contact services
4
Food equipment installation
Notes: 2

## Slide 3: SANITARY CONSTRUCTION & DESIGN OF FOOD EQUIPMENT
General Aspects
The surfaces of food equipment can be subdivided into two categories:
  Food product contact surfaces, and
  Non-product contact surfaces.
Food product contact surface: A surface in “direct contact with food residue, or where food residue can drip, drain, diffuse, or be drawn”
Non-product contact surface: Those surfaces that are part of the equipment (e.g., legs, supports, housings) that do not directly contact food.
Notes: 3

## Slide 4: FOOD PRODUCT CONTACT SURFACES
In terms of sanitary design, all food contact surfaces should be:
Smooth
Impervious
Free of cracks and crevices
Nonporous
Nonabsorbent
Non-contaminating
Nonreactive
Corrosion resistant
Durable and maintenance free
Nontoxic
Cleanable
Notes: 4

## Slide 5: FOOD PRODUCT CONTACT SURFACES
In terms of sanitary design, all food contact surfaces should be:
If the surface is coated with metal alloy or non-metal (e.g. ceramics, plastic, rubber) in any way, the final surface must meet the above stated requirements.
Such coatings should maintain corrosion resistance, and be free of surface delamination, pitting, flaking, chipping, blistering, and distortion under conditions of intended use
If any other modification or process is used in fabrication (e.g., welded, bonded, or soldered) it should be done using appropriate materials and in a manner that ensures the final surface meets the sanitary design criteria.
Focus areas
  Materials
  Surface texture/ finish
  Construction & fabrication
Notes: 5

## Slide 6: Food product contact surfaces
Materials- Metals
A variety of materials are used in the construction and fabrication for different applications in food equipment. These materials vary in their properties with regard to workability, compatibility, and sanitary design features.
Metals:
  Stainless steel is the preferred general use metal for food contact surfaces because of its corrosion resistance and durability in most food applications
  Titanium has excellent durability and corrosion resistance (especially in an acidic environment) . However, its use is limited by high cost. Titanium is used in stainless steel alloys for food equipment used in the processing of food products with high acid and/or salt content (e.g., citrus juice, tomato products).
Notes: 6

## Slide 7: FOOD PRODUCT CONTACT SURFACES
Materials- Metals
Metals limited by application:
  Copper is primarily used for equipment used in the brewing industry, with some use for cheese vats in Swiss cheese manufacture, due to tradition. Care should be used with copper equipment when processing acid products, as copper residues can leach into the product.
  Aluminum is used in certain parts and components where lighter weight is desired. However, aluminum has poor corrosion resistance and can become pitted and cracked with continued use. Care should taken when cleaning and sanitizing aluminum components as oxidizing chemicals can accelerate the pitting of the metal.
  Carbonized metal and cast iron are only used for frying and cooking surfaces, and similar applications in food service.
  Galvanized iron should be avoided as a food contact surface because it is highly reactive with acids.
Notes: 7

## Slide 8: FOOD PRODUCT CONTACT SURFACES
Materials- Non-metals
Non-Metals
  Plastics, rubber, and rubber-like materials that should be food grade
  Ceramics are used primarily in membrane filtration systems. They may also be used in other limited applications if wear resistance is necessary.
  Glass may be used as a food contact surface. These applications are limited due to the potential for breakage. When glass is used, it must be durable,break resistant or heat resistant glass. Some applications where glass is used are light and sight openings into vessels and in very limited glass piping applications.
  Paper has been used over the years as a gasket material in piping systems designed for daily disassembly. Paper is considered a single use material.
  Wood, which is highly porous and difficult to clean, should be avoided as a food contact surface.
Notes: 8

## Slide 9: FOOD PRODUCT CONTACT SURFACES
Surface Texture and/or Finish
If any surface is ground, polished, or textured in any way, it must be done so the final surface is smooth, durable, free of cracks and crevices
polished stainless steel surfaces meet a No. 4 ground surface, and unpolished surfaces meet a No. 2B or mill finish.
The surface texture or finish of a material is decided by Ra Value
  Roughness average or Ra value is determined using a sensitive instrument (termed a profilometer) which employs a diamond tipped stylus to measure peaks and valleys in a relatively smooth surface
Notes: 9

## Slide 10: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Food equipment should be designed and fabricated in such a way that all food contact surfaces are free of sharp corners and crevices.
All mating surfaces must also be continuous (e.g., substantially flush).
Construction of all food handling or processing equipment should allow for easy disassembly for cleaning and inspection
Where appropriate (e.g., vessels, chambers, tanks), equipment should be self-draining and pitched to a drainable port with no potential hold up of food materials or solutions
Notes: 10

## Slide 11: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Acceptable vs. unacceptable self-drainage design for tanks and vessels
Notes: 11

## Slide 12: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Piping systems not designed for routine disassembly must be sloped to drain
Drainage of Pipes
Notes: 12

## Slide 13: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Internal Angles
  Should be coved or rounded with defined radii
  Equipment standards specify appropriate radii for specific equipment applications and components. For example, radii requirements stated in the 3A Sanitary Standards indicate that “all internal angles 135 degrees or less should have a minimum radii of 1/4 inch (6.35 mm).”
Acceptable vs. unacceptable internal angles of food equipment
Notes: 13

## Slide 14: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Permanent Joint
  All joints should be smooth, durable, and meet all sanitary design criteria.
  Equipment standards generally require that welded joints on stainless steel surfaces be continuous, butt-type joints and ground smooth
Permanent welded joints showing butt weld vs. lap weld
Notes: 14

## Slide 15: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Permanent Joint
  If the welded joint is at a corner, it must be coved to the appropriate radius and ground smooth
  Use of soldered joints should be limited by application with use of only non-toxic materials
Corner welds in food equipment
Notes: 15

## Slide 16: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Connections, attachments, and ancillary equipment
  Care should be taken when connecting pipes, gauges, thermometers, probes, or other equipment to food contact surfaces.
  It is necessary to ensure the connection does not create a dead end or an area where food product can accumulate and is not accessible to cleaning solutions
  Such connections should be close coupled (e.g., pipe connection should not be of length greater than one pipe diameter)
Notes: 16

## Slide 17: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Connections, attachments, and ancillary equipment
Closed connection length (a) no greater than the pipe diameter (d)
Notes: 17

## Slide 18: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Connections, attachments, and ancillary equipment
Acceptable vs. un acceptable gauge connections
Notes: 18

## Slide 19: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Connections, attachments, and ancillary equipment
  Shafts, bearings, agitators, and other attachments or ancillary components should be attached to food equipment in such a way that the food contact zone is sealed from contamination caused by leakage of lubricants or other contaminants into the product zone.
  Such components should be accessible and removable for cleaning. Threads of food equipment are to be avoided in or over the food product zone.
Notes: 19

## Slide 20: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Openings, covers, and top rims
  Any opening or cover should be designed, fabricated, and constructed in such a manner as to adequately protect food products from contamination and to divert potential contamination away from the food product zone.
  Openings should be lipped and covered with a shoe box type design and the top rims of equipment should be constructed and fabricated to avoid the collection of water droplets or dust.
Notes: 20

## Slide 21: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Openings, covers, and top rims
Acceptable shoe box design openings and covers
Notes: 21

## Slide 22: FOOD PRODUCT CONTACT SURFACES
Construction and Fabrication
Openings, covers, and top rims
Top rim of food equipment
Notes: 22

## Slide 23: NON-FOOD PRODUCT CONTACT SURFACES
Non food contact surfaces
Non-product contact surfaces of food equipment are a source for environmental contamination of a food facility with pathogens (especially Listeria monocytogenes).
These areas can also be harborage areas for insects and rodents. Therefore, care should be used in evaluating these surfaces of equipment with regard to sanitary construction and design.
non-product surfaces of equipment should be constructed with appropriate materials and fabricated in such a manner as to be reasonably cleanable, corrosion resistant, and maintenance free.
Tubular steel equipment framework should be entirely sealed and not penetrated (e.g., bolts, studs), to avoid creating niches for microorganisms
Whenever practicable, attachments should be welded to the surface of the tubing and not attached via drilled and tapped holes.
Notes: 23

## Slide 24: NON-FOOD PRODUCT CONTACT SURFACES
Non food contact surfaces
Tubular framework with bolted attachments potential microbial niche
Notes: 24

## Slide 25: FOOD EQUIPMENT INSTALLATION
Food equipment should be
Installed in a logical sequence top avoid cross contamination
Space around and between equipment and between equipment, and walls should be adequate enough to allow for sufficient cleaning
There should be no potential harborages for insects and rodents.
Unless sealed to walls, food equipment should be at least 4 inches from walls.
Floor mounted equipment should be sealed to the floor, platform, or pedestal or should be no less than 6 inches from the floor.
Table mounted equipment should be sealed to the table, or be no less than 4 inches from the counter top
Notes: 25

## Slide 26: FOOD EQUIPMENT INSTALLATION
Food equipment should be
Floor mounting of stationary food equipment
Notes: 26