## Slide 1: INTEGRATED PEST MANAGEMENT

## Slide 2
1
AGENDAITEMS
Integrated pest management
2
What pests do?
3
Pests in a food facility
4
Pest harbourage- “Hot spots”
5
Elements of integrated pest management
6
Pest control techniques

## Slide 3
INTEGRATED PEST MANAGEMENT
Integrated pest management
An ecosystem based strategy focusing on long term prevention of pests & their damage.
The three basic steps of IPM:
  Inspection
  Identification
  Treatment
Need for IPM
Without an effective pest management program in place, insects & rodents can infiltrate the food facility, leading to
  Food contamination,
  Product recalls
  Several health threats.

## Slide 4
INTEGRATED PEST MANAGEMENT
Integrated pest management
An ecosystem based strategy focusing on long term prevention of pests & their damage.
The three basic steps of IPM:
  Inspection
  Identification
  Treatment
Need for IPM
Without an effective pest management program in place, insects & rodents can infiltrate the food facility, leading to
  Food contamination,
  Product recalls
  Several health threats.

## Slide 5
WHAT PESTS DO?MS
Production area
Contaminate Food ( droppings  bacteria)*
Spoil food by eating parts of it
Cause damage to equipment
Carry disease
Hamper normal plant functioning
Warehouse and storage
Cause damage to raw materials and finished products
Damage packaging materials
Create unhealthy environment
Play as carrier for pathogens

## Slide 6
PESTS IN A FOOD FACILITYS
Hazards
Damage to buildings and fixtures
Damage to machinery leading to production downtime
Contamination along access routes with urine, droppings, and filth picked up from the environment
damage to food containers and packaging
Transmission of diseases (Salmonellosis, Leptospirosis, Toxoplasmosis, Lyme disease, rat-bite fever)
Signs
Sightings of live or dead animals
Droppings
Smudge marks along runs caused by their oily fur
Gnawing of building materials, wiring, food and packaging
Noises: squeaks, gnawing sounds, scurrying sounds
Rodent Pests(rat & mice)

## Slide 7
PESTS IN A FOOD FACILITYS
Hazards
Diseases and allergens: cockroaches can carry a large number of disease-causing bacteria, including Salmonella, Staphylococcus, Listeria, E. coli, and also fungi, viruses and parasitic worms;
Cast skins and egg cases contaminate products and packaging
droppings and bodily secretions stain and leave a foul odor that can permeate infestation areas, food and packaging
Signs
Sightings of cockroach adults & nymphs
Body parts such as legs, antennae, etc.
Egg casings & cast skins
Small, dark fecal spots may indicate areas of activity or entrances to hidden harborages.
Insect Pests(cockroaches & flies)

## Slide 8
PEST HARBORAGE- “HOT SPOTS”
Hot Spots
Places to look out for
Certain areas that pests tend to target.
Entrances
Use door sweeps to minimize gaps
Install autoclosing doors
Use of HVAC systems
Receiving & Storage
Exterior receiving doors to seal tightly
Inspect all shipments for signs of pests, damaged packaging etc.
Dispose empty CFB’s
Outside
Add two foot gravelstrip between bushes and wall of plant.
No plants/ shrubs to touch building
Use Cu mesh around pipes
Inside
Repair cracks and cervices in facility
Empty trash cans & clean spills
Follow sanitization schedule
Machinery areas
Avoid equipment squeezing into tight areas
Minimize liquid accumulation within the equioment as well as on the plant floor.

## Slide 9
ELEMENTS OF INTEGRATED PEST MANAGEMENT
Building & materials
Facility & equipmenty should not promote pest populations
Should be amenable to control and treatment methods.
Exclusion practices
Raw material should be received in a building that is separate from the main processing facility
Treat materials before they enter main process flow.
Good Sanitation Practices
Cleaning must be conducted thoroughly, regularly and frequently, with written procedures identifying cleaning methods.
Building maintenance
Holes and cracks in floors, walls, ceilings, roofs, doors and windows allow access for vermin and allow dust to collect, and therefore must be fixed
Inspection & monitoring
Monitoring program should include establishment of targets and action levels, and schedules for placing and checking traps or other techniques
Pest identification
Accurate identification of pests is necessary to select the most appropriate control methods.

## Slide 10
PEST CONTROL TECHNIQUES
Methyl Bromide
Used for plant fumigations
A combination of methods, used together or at different times, might be required, along with the other components of an IPM strategy.
The choice of treatment is situation specific to deal with specific problems, and can range from spot treatments to full site treatments as necessary.
Baiting & Trapping
Insect baits:
  Insect baits are available for cockroaches and ants.
Pheromone traps have also been used in a few places to reduce insect populations
Rodent Baits:
  To be used outdoors and placed in tamper proof bait stations
  Secure to building exteriors & mark location on map
Physical & Chemical Controls

## Slide 11
PEST CONTROL TECHNIQUES
Natural/synthetic organphosphate
Frequent application method is applying the pesticide as small particles in an air suspension (Ultra Low Volume method)
ULV is effective in rapid knock down of flying insects such as Indian meal moths, tobacco moths, and flies.
Crack & Cervice treatment
It refers to the use of a liquid or aerosol formulation of insecticide
The material is applied in small amounts to likely harborage areas or areas where infestation has been noted.
The insecticides applied may have either a residual or non-residual activity.
Physical & Chemical Controls

## Slide 12
PEST CONTROL TECHNIQUES
Exterior Treatments
This involve applications of residual insecticides to thresholds, the foundations and soil adjacent to the foundation
This method is useful in controlling some outdoor insects, which can occasionally become a nuisance or invade if the population builds up.
Products used could be synthetic pyrethroids, chlorpyrifos in liquid or granular form, or diazinon in liquid or granular form.
Heat Treatment
It generally requires achieving a temperature of 51°C to 57° C for a period of 24 hours.
Heat treatments are most feasible where existing in-plant heat sources can be used
Uniform air circulation to distribute heat through the facility is critical.
Equipment/products susceptible to heat damage must be removed, stored in air conditioned rooms, or insulated during the treatment.
Physical & Chemical Controls

## Slide 13
PEST CONTROL TECHNIQUES
Low Temperatures
This can be used to reduce the development rate, feeding, and fecundity of insects & reduce their survival
Primarily for bulk storage, either through refrigeration or exposure to ambient air in colder climates.
Temperatures needed to control insects are -20°C for 1 minute, -10°C for 1-7 days, or 0°C for 1 week to 1 month, depending on the type of pest & rate of cold penetration of all areas of the facility
Phosphine Gas
Phosphine gas is generated by the reaction of metallic phosphide with atmospheric moisture
Used on its own, relatively high concentrations and long exposure times are required, for example, initial dosages of 900 to 1200 ppm and final concentrations of 200 to 400 ppm for 36 to 48 hours
Physical & Chemical Controls