## Slide 1
MATERIAL HANDLING

## Slide 2
ABOUT PMG
At PMG, we deliver Engineering Design and Project Management scopes in Food and Beverage industry. Our team of design engineers and engineering executives has rich experience in Project Planning, Design, Execution and Commissioning with key competencies in areas like 3D Plant Design, Hygienic Engineering, and Project Management. Our safe-by-choice, result-oriented, and pro-active work-ethics allow us deliver work scopes meeting objectives, complete stakeholder alignment and first-time quality.
PMG Knowledge Repository: Targeted Knowledge Sharing & Skill Development
Precise and focused training modules for the exhaustive set of people working in manufacturing industry, instilling qualities of self-belief, creative thinking & widened perspective.
“BUILDING FOOD FACTORIES WITH TOP QUALITY STANDARDS OF NESTLE, MONDELEZ,ABBOTT, DANONE USING 3D DESIGN AND HYGIENIC ENGINEERING.”
Clear Learning Objectives
Focused approach to skill development and knowledge sharing
Progressive Evaluation
Gauging improvement on every step and keeping audience connected.
After-training follow-ups
We systematically track differential progress of recipients after the training.
Audience Specific Approach
Programs are fine-tuned to the ability and interests of the recipients.
Multiple Awe-moments
Awe-moments are refreshing and increase receptivity many-fold.
Seasoned Trainers
PMG trainers are subject matter experts with substantial work experience.

## Slide 3: AGENDA
2
Definitions
3
Objectives of material handling
4
Reduce manufacturing cycle time
5
Limitations of automated material
6
Risk assessment & management
7
Design of MHE routes
1
Induction
Notes: 3

## Slide 4: AGENDA
9
Mhe requirements & maintenance
10
Operating procedures & behaviours
11
Incident investigation, performance monitoring & auditing
12
Definitions of key terms
8
Traffic route conditions
Notes: 4

## Slide 5
Material handling is a necessary and significant component of any productive activity. It is something that goes on in every plant all the time. Material handling means providing the right amount of the right material, in the right condition, at the right place, at the right time, in the right position and for the right cost, by using the right method.
INDUCTION

## Slide 6
There are many ways by which material handling has been defined but one simple definition is “Material handling is the movement and storage of material at the lowest possible cost through the use of proper method and equipment”.
DEFINITIONS

## Slide 7
The primary objective of a material handling system is to reduce the unit cost of production. The other subordinate objectives are:
  Reduce manufacturing cycle time
  Reduce delays, and damage
  Promote safety and improve working conditions
  Maintain or improve product quality
  Promote productivity
  Promote increased use of facilities
  Reduce tare weight
  Control inventory
OBJECTIVES OF MATERIAL HANDLING

## Slide 8
Cost of material handling equip
Cost of labor
Cost of maintenance equipment
Material handling system
Both fixed cost and operating cost calculated as cost of equipment divided by the number of units of material handled over the working life of the equipment
Damages, lost orders and expediting expenses, also calculated, in terms of cost per unit of material handled.
Damages, lost orders and expediting expenses, also calculated, in terms of cost per unit of material handled.
Reduced Manufacturing Cycle Time
Both direct and indirect associated cost calculated in terms of cost per unit of material handled.
REDUCE MANUFACTURING CYCLE TIME

## Slide 9
A good management practice is to weigh benefits against the limitations or disadvantages before contemplating any change. Material handling systems also have consequences that may be distinctly negative. These are:
  Additional investment
  Lack of flexibility
  Vulnerability to downtime whenever there is breakdown
  Additional maintenance staff and cost
  Cost of auxiliary equipment
  Space and other requirements
LIMITATIONS OF AUTOMATED MATERIAL

## Slide 10
Overview of risk management
Risk assessment of shared areas
Sites must control risks associated with MHE to prevent injuries, illnesses or property damage:
  Wherever feasible, the potential for harm must be eliminated or reduced
  Residual risks must be controlled through engineering, procedural and behavioural measures. Priority must be given to the measures which are most reliable.
In the case of internal shared areas (i.e. areas within buildings where PITs and pedestrians could both be present at the same time), an additional assessment must be carried out using the PIT/Pedestrian Risk Assessment Tool and action plans developed to address identified risks
RISK ASSESSMENT & MANAGEMENT

## Slide 11
Material Handling Equip- routes must
In addition, for pits,
Be of sufficient size to enable the safe passage of MHE
Avoid vulnerable items and locations
Maximize visibility for operators and pedestrians
PITs must be physically separated from pedestrian routes and work stations
Reversing must be minimized
DESIGN OF MHE ROUTES

## Slide 12
MHE traffic routes must be
Critical locations on MHE routes
Of appropriate construction for the intended use
Provided with appropriate markings
Maintained in good physical condition
Sufficiently well-lit to enable MHE and pedestrians to move around safely
Kept free from obstructions, debris, leaks, and spills.
Risk assessments must identify locations where risks of MHE collision are most significant: with Pedestrians, with other MHE, and with other plant and equipment. Such locations must have special controls in place. Structural supports and racking must be provided with physical protection to prevent damage, unless the risks of collision (or consequences of damage) are insignificant.
TRAFFIC ROUTE CONDITIONS

## Slide 13
Safety distance rule
Speed of pits & AGVs
Sites must implement a safety distance rule around PITs and Automatic Guided Vehicles when they are in operation1. In the case of PITs, the safety distance must be at least 3m. Situations where the rule cannot be complied with must be recorded and highlighted to local management for review.
The speed of PITs and AGVs must be carefully managed to help minimize risk of collisions and other incidents.
TRAFFIC ROUTE CONDITIONS

## Slide 14
MHE routes must
MHE must be suitable for its intended task and working environment, and must not be loaded beyond its safe working load. Furthermore, all PITs must be fitted with:
  A horn
  Seat belts (unless the operator position is standing)
  Devices to prevent unauthorised use
  Information on the safe working load
MHE REQUIREMENTS & MAINTENANCE

## Slide 15
Automatic Guide Vehicle System must be fitted with
A visible warning device.
A safety-rated personnel detection and braking system.
An emergency stop control.
MHE REQUIREMENTS & MAINTENANCE

## Slide 16
MHE REQUIREMENTS & MAINTENANCE
MHE routes must
Maintenance of MHE
Attachments must only be put into use after a competent person has assessed their compatibility. Any required de-rating must be marked on the relevant MHE. MHEs must only be used to lift people if no safer alternative is available. If people are lifted, this must be done using an appropriate work platform, securely attached to the MHE.
MHE must be maintained in good working order through a combination of pre-use inspections by MHE operators, and planned and breakdown maintenance by competent technicians. If faults are identified which affect the safety of operation, the MHE must not be used until the fault is corrected.

## Slide 17
Procedures & rules
Work with AGVS
Vehicle loading & unloading
MHE battery charging
Site management must establish standard operating procedures for use of MHE. This must include site rules and behavioural expectations for relevant staff
Prevent drive-away during external/side loading and unloading;
Ensure the safety of visiting drivers, particularly from collisions with MHEs
Within a designated, well-ventilated area
In accordance with a standard operating procedure.
Interventions with AGVs must only be done by specially trained personnel, and only after stopping the AGV using the stop control and/or emergency stop control.
OPERATING PROCEDURES & BEHAVIOURS

## Slide 18
OPERATING PROCEDURES & BEHAVIOURS
PPE
Behaviours of MHE operators
Safety shoes must be worn in all production, logistics and utilities areas
High visibility clothing must be worn in all PIT/Pedestrian shared areas
Wear the defined PPE
Operate the MHE as per the training received and local procedures
Wear the seat belt when fitted
Be mindful of the surroundings and apply the safety distance rule
Disable powered MHE before leaving it, to prevent unauthorised use
Report all incidents, collisions and near misses

## Slide 19
Behaviours of pedestrians
Wear the defined PPE;
Minimize the time spent in PIT/pedestrian shared areas;
Be mindful of the surroundings and apply the safety distance rule;
Never stand or walk under a raised load;
Use marked walkways and pedestrian crossings;
Report all incidents, collisions and near misses.
OPERATING PROCEDURES & BEHAVIOURS

## Slide 20
Behaviours of team leaders & managers
Ensure risk assessments are carried out and required controls are implemented
Ensure staff receive adequate MHE-related training
Monitor compliance with safety procedures, and challenge and coach those who do not follow procedures
Encourage the team to discuss MHE risks, and to identify and address unsafe conditions and at-risk behaviours
Act as a personal role model for operator and pedestrian behaviours
OPERATING PROCEDURES & BEHAVIOURS

## Slide 21
Operator authorization
Before authorizing personnel to operate MHE, site management must ensure they have received adequate training on the specific MHE to be used, as well as site-specific hazards, rules and procedures. In the case of PITs, workers must also have been:
  Certified as competent to operate the relevant type/model of PIT.
  Assessed as fit-to-operate by a health professional.
  Training and certification of PIT operators must be carried out by competent instructors.
  PIT operators must be re-certified for competency, and reassessed for fitness-to-operate, at least every 3 years.
OPERATOR SELECTION & TRAINING

## Slide 22
Training for managers & team leaders
Managers and team leaders with responsibility for operations involving MHE must have sufficient appreciation of the associated risks and control measures to enable them to effectively supervise the work. Training must include:
  The risks associated with the MHE and associated activities;
  The precautions to be taken;
  Relevant legal requirements;
  Their responsibilities and required behaviours
OPERATOR SELECTION & TRAINING

## Slide 23
INCIDENT INVESTIGATION, PERFORMANCE MONITORING & AUDITING
Incident reporting & investigation
Performance monitoring & auditing
Incidents involving MHEs must be investigated to understand what can be done to minimise the chance of recurrence. Where appropriate, corrective and preventive actions must be implemented
In addition, the site’s management of MHE risks must be regularly audited to:
  Assess compliance with legal and Company requirements;
  Review the effectiveness of the current arrangements;
  Identify opportunities to further improve management of the identified risks.

## Slide 24
DEFINITIONS OF KEY TERMS
AGV - automatic guided vehicle
MHE – material handling equip.
Any rider-less form of MHE, designed to travel automatically along a pre-defined route1.
Some types of AGV have additional functionality, eg:
Automatic load handling, which enables the AGV to pick up and manoeuvre loads using forks, clamps, etc
Ability to pull non-driven carts with loads
Any moveable equipment used to transport materials around a facility. It excludes mobile cranes and hoists but includes rider-controlled equipment (PITs), automatic rider less equipment (AGVs), and pedestrian-controlled equipment

## Slide 25
DEFINITIONS OF KEY TERMS
Pit – powered industrial truck
Pedestrian
Any rider-controlled form of MHE. It includes counterbalance fork lift trucks, reach trucks, order picking trucks, etc.
Any person standing or walking in a work area.

## Slide 26
Shared area
Any work area in which PITs and pedestrians could both be present at the same location at the same time, thereby creating a collision risk. This includes demarcated pedestrian walkways without physical barriers.
DEFINITIONS OF KEY TERMS

## Slide 27
Our Clients